## Slide 1
by Nick Mark MD
minnesota tubes for upper gi bleeds
onepagericu.com
@nickmmark
Link to the most current version →
ONE
PURPOSE:
Minnesota tubes (MT) are typically placed in intubated patients with life-threatening GI hemorrhage (particular esophageal varices) when interventional approaches to control hemorrhage have been unsuccessful or are unavailable.
The MT is a four-lumen gastric tube that permits tamponade of gastric and esophageal bleeding as well as continuous aspiration of gastric & esophageal contents. It is an improvement over the older Sengstaken–Blakemore tube (SBT), which only permitted gastric contents to be aspirated.
Endotracheal intubation with HOB >45° is recommended prior to MT placement.
ESOPHAGEAL balloon port
Suction canister
GASTRIC aspiration port
GASTRIC balloon port
ESOPHAGEAL aspiration opening
ESOPHAGEAL balloon directly compresses varices
GASTRIC balloon compresses the GE junction reducing blood flow to esophageal varices
GASTRIC aspiration openings
200
400
600
800
1000
1200
1400
PLACEMENT: (excellent step by step videos are also available)
1 kg weight traction
(prevents the MT from sliding in too deep)
Test the balloons by inflating and submerging underwater to ensure no leaks. Attach the sphygmomanometer/syringe GASTRIC balloon port and inflate to 100, 200, and 500 cc (note the pressure at each volume). Completely deflate the balloons after testing. Lubricate the distal 15 cm of the MT prior to insertion.
Measure from the mouth to ear to xiphoid process and insert the tube through the mouth to that depth. Use a video laryngoscope to help guide MT insertion into the esophagus.
Insert MT to the measured distance + 10 cm (typically about 50-60 cm) & verify placement:
GENERAL RULES:
ESOPHAGEAL aspiration
port
Instill 50-100 cc of air into the GASTRIC port & obtain CXR
POCUS can also be used to confirm the presence of MT in the stomach.
If imaging confirms gastric placement of MT, continue to inflate to 300-500 mL
If pressure rises above 15 mmHg STOP
Once placement is confirmed, connect gastric aspiration to intermittent suction (negative 60-120 mmHg). Clamp the gastric balloon port. Assess for ongoing bleeding.
In the majority of cases the gastric balloon is able to control hemorrhage. However, if bleeding continues, inflate the ESOPHAGEAL balloon to tamponade varices further.
Always INFLATE the GASTRIC balloon first
Always DEFLATE the ESOPHAGEAL balloon first
If there’s a doubt about placement, repeat CXR
Never exceed 15 mmHg with the GASTRIC balloon or 45 mmHg with the ESOPHAGEAL balloon
Never irrigate the ESOPHAGEAL suction port
Instill 50cc of air at time and measure pressure.
Goal is 25-40 mmHg of ESOPHAGEAL pressure (higher can cause esophageal erosion).
Clamp the ESOPHAGEAL balloon. Obtain CXR.
Connect the ESOPHAGEAL port to continuous wall suction at negative 120-200 mmHg.
60 cc syringe
Manometer allow pressure monitoring
Y-connector
Rubber lined hemostats are used to clamp the tube
OFF
INT
CON
Wall suction regulator
Pilot balloon indicates that ESOPHAGEAL balloon is deflated
Controls determine intermittent or continuous suction & the pressure applied
CC BY-SA 3.0
v1.0 (2021-01-29)
The distance from mouth to ear to xiphoid approximates the distance from the mouth to the stomach
Mark the tube at the lips & record depth. Secure the tube w/ a 1 kg weight for traction. A catcher’s mask can also be used.
If bleeding resolves, DEFLATE the ESOPHAGEAL balloon by 5 mmHg every 3 hours until completely deflated.
If no bleeding recurs for 24 hours, release traction & deflate the GASTRIC balloon.
If no bleeding for another 24 hours, remove the MT.
REMOVAL:
Use 2 suction setups
(1 for each port)