## Slide 1
by Nick Mark MD
overview of ventilator modes
onepagericu.com
@nickmmark
Link to the most current version →
ONE
Mode | Description | Pro’s | Con’s | Major settings / example | Monitor
VC Volume Control (a.k.a. assist control volume) | Every breath delivered (mandatory and patient triggered) are all the same set volume | Good general-purpose mode; Ensures a minimum MV is achieved. Good mode for lung protective ventilation (LPV) | Requires you to monitor pressures to avoid barotrauma. (See my OnePager on ARDS for details.) | RR, TV, PEEP, FIO2 | Pressures (Ppeak, Pplat)
 | T – time/pressure/flow, C – volume, L – volume |  |  | 12 bpm, 450cc, +8, 60% | 
PC Pressure Control (a.k.a. assist control pressure) | Every breath delivered (time & patient) are a set pressure for a set time | Good for limiting pressure; may be more comfortable for select patients. Also can be used for LPV (no difference in mortality) | Requires you to monitor volumes to avoid volutrauma or hypoventilation | RR, IP, TI, Risetime, PEEP, FIO2 | Volumes (TV, MV)
 |  |  |  | 12 bpm, 25 cmH2O, 0.9 sec, 0.15 sec, +8, 60% | 
 | T - time/pressure/flow, C – time, L - pressure |  |  | 12 bpm, 25 cmH2O, 0.9 sec, 0.15 sec, +8, 60% | 
PRVC Pressure Regulated Volume Control (a.k.a. VC+) | Hybrid PC mode that dynamically changes inspiratory pressure to deliver a desired volume | Guarantees TV but delivers pressure-controlled breaths; (e.g. low risk of causing VILI), which potentially may be more comfortable for patients | In patients who are struggling to breath the machine will provide less support | RR, TV, TI, Risetime, Pmax, PEEP, FIO2 | Pressures & volumes
 | T - time/pressure/flow, C – volume, L - volume |  |  | 12 bpm, 450cc, 0.9 sec, 0.15 sec, 30 cmH2O, +8,60% | 
SIMV Synchronous Intermittent Mandatory Ventilation | Delivers mandatory breaths with a fixed volume but patient can’t trigger (patient breaths are not the same as mandatory breaths); can use PS | May be useful for patients with hiccups to avoid alkalemia | Seldom used; not effective for weaning; often found to be uncomfortable | RR, TV, PEEP, FIO2 | Pressure (Ppeak Pplat)
 | T – time , C – volume, L - volume |  |  | 12 bpm, 450 cc, +8, 60% | 
PS Pressure Support | All breaths are patient initiated; ventilation determined solely by patient (no backup rate). | Ideal weaning mode (used in SBTs and for prolonged periods); most comfortable because it allows patient to control ventilation | Does not guarantee a rate; need to monitor to ensure adequate ventilation | PS, PEEP, FiO2 | Volumes (TV, MV)
 | T – pressure/flow, C – flow, L - pressure |  |  | +10, +5, 40% | 
APRV Airway Pressure Release Ventilation (a.k.a. Bi-Vent) | Inverse ratio ventilation (e.g. I time > E time) that allows patient to breath spontaneously; can combine w/ PS | Great for ARDS patients who are spontaneously breathing (e.g. not on NMB); may improve comfort & oxygenation (but no mortality benefit) | Complex mode/settings; Risk of VILI if settings are done improperly; doesn’t make sense if on NMB | THigh, TLow, Phigh, Plow, FIO2 | Volumes & gas exchange PCO2 / EtCO2
 |  |  |  | 5.5 sec, 0.5 sec, 25 cmH2O, 0 cmH2O, 60% | 
 | T – time, C – time, L - pressure |  |  | 5.5 sec, 0.5 sec, 25 cmH2O, 0 cmH2O, 60% | 
pH / PCO2 / PaO2 / HCO3 SpO2
VENTILATION
OXYGENATION
If you want to increase the pH  increase the ventilation parameters
If you want to change the PaO2 or SpO2 adjust oxygenation parameters (FiO2 and PEEP)
Goals for mechanical ventilation:
Oxygenation – support PaO2/SpO2
Ventilation – maintain pH
Patient comfort – vent synchrony, ↓ sedation
Facilitate weaning – minimize muscle loss, promote readiness to wean from support
Measure
ABG/SpO2
Adjust
Settings
ABG
Pulse Ox
Define treatment goals
Choose a ventilator mode & initial settings
Measure ABG/VBG/Spo2
Ask am I achieving my goals?
Adjust Settings
Try a different mode
If unable to achieve, can redefine goals (e.g. permissive hypercapnia)
Ventilator Modes:
Fall into two broad categories: pressure and volume modes. Each mode has three features:
Trigger (T) – what initiates a breath?
Cycle (C) – what ends a breath?
Limit (L) – what stops a breath early?
Each mode has Pro’s and Con’s to consider.
Note that PS is above PEEP so “Ten over Five” PIP = 15cmH2O
Try adjunct
(sedation, NMB, bronchodilator, etc)
(Thigh/low – time high/low, Phigh/low – pressure high/lowNote that Plow is analogous to PEEP)
Measurement and optimization:
(RR – respiratory rate, TV – tidal volume)
(IP – inspiratory pressure, TI – inspiratory time)
(Pmax – maximum pressure)
v1.0 (2020-04-03)