## Slide 1
Pressure transducer
‘Zero’ level is the mid-axillary line. (do NOT use the phlebostatic axis or the symphysis pubis as these underestimate the true pressure)
IV fluid in pressure bag at 300 mmHg
60 mL Syringe
50
100
150
200
250
Padded hemostat used to temporarily clamp Foley during measurement
Foley catheter
Foley bag & urimeter
18 Fr
Intra-Abdominal Pressure
Bladder Pressure
≃
(this is only true if the bladder is completely drained & abdominal muscles relaxed)
abdominal compartment syndrome
Link to the most current version →
ONE
DEFINITIONS:
by Mark Ramzy DO & Nick Mark MD
Improve Abdominal Wall Compliance
Abdominal wall compliance is often increased due to increased muscle tone, often due to pain or anxiety
- Ensure adequate sedation and analgesia
- Avoid abdominal binders or restrictive bandages
- Place in Reverse Trendelenburg if able
- Consider neuromuscular blockade
Optimize Fluid Status
Volume overload exacerbates gut and abdominal wall edema and may cause intra-abdominal fluid accumulation.
- Minimize IVF, stop MIVF, avoid aggressive fluid resuscitation,
- Aggressively diuresis if needed and able to tolerate
- Goal is net even to negative fluid balance
- RRT (Ultrafiltration) may be required
See Achieving a Negative Fluid Balance OnePager for more
Surgical Decompression
Severe cases require surgical decompression
- Full midline laparotomy from xiphoid to pubis is common
- Earlier intervention shown to improve outcomes
- Even with an open abdomen, ACP can recur; watch for severe fluid loss & use goal-directed fluid resuscitation & monitor hemodynamics to maintain MAP & APP
Evacuate Intraluminal Content
Removal of content from the gut reduces IAP; Gastroparesis, ileus, and colonic-pseudo-obstruction are common causes, especially in patients who are post-op.
- Place a gastric tube to decompress stomach
- Stop enteral feeds if ongoing
- Consider prokinetic agents (e.g. Metoclopramide), administration of enemas, and endoscopic decompression
Intra-Abdominal Pressure (IAP) is the pressure within the abdomen, reflecting the outward pressure of abdominal contents & inward pressure of the abdominal wall
Intra-Abdominal Hypertension (IAH) is IAP (>12 mmHg) due to underlying pathology
Abdominal Compartment Syndrome (ACS): is the physiologic consequence of an IAP >20 mmHg causing organ dysfunction; it also compromises venous return to the heart (reduced CO) and impedes lung expansion. ACS can be divided into Primary (due to organ edema, pancreatitis, accumulation of intrabdominal or retroperitoneal fluid, etc), Secondary (due to sepsis, excessive fluid resuscitation, circumferential abdomen burns, etc), Chronic (due to long standing ascites, mass, Meig’s syndrome, peritoneal dialysis, etc), & Recurrent (development of ACS after previous treatment)
ABDOMINAL PERFUSION:
Abdominal
perfusion
pressure
Mean arterial pressure
Intra-abdominal pressure
Normal APP ≥ 60 mmHg
LESS than 60 predicts need for surgical decompression
Maintaining a MAP ≥ 65mmHg normally ensures adequate end-organ perfusion
Normal = 0 – 5 mmHg
ICU pts = 5 – 7 mmHg
IAH ≥ 12 mmHg
Grade I: IAP 12-15 mmHg
Grade II: IAP 16-20 mmHg
Grade III: IAP 21-25 mmHg Grade IV: IAP >25 mmHg
MEASURING BLADDER PRESSURE AS A SURROGATE FOR IAP
CC BY-SA 3.0 v1.0 (2021-02-07)
onepagericu.com
@MRamzyDO
@Nickmmark
1. Place the patient in a supine position
2. Ensure correct placement (e.g. POCUS) and function of Foley urinary catheter (e.g. flushes)
3. Connect a transducer, flush syringe, and pressure bag to the Foley side port
4. Zero the transducer at the level with the mid-axillary line
5. Clamp catheter distal to the port with a padded hemostat
6. Turn the stopcock off to the patient allowing syringe to fill with IV fluid from pressure bag
7. Turn the stopcock back on to patient and inject the filled syringe into bladder
8. Release hemostat clamp on foley to allow flushing of air from the urinary catheter
9. Wait up to 1 minute to allow bladder detrusor muscle relaxation to occur
10. Measure IAP in end-expiratory phase either continuously or every 4 – 6 hours
Indirect measurements of IAP include measuring IVC, intragastric or intrauterine pressure. Intra-vesicular pressure is the most straightforward & minimally invasive method though it does slightly overestimate true intra-abdominal pressure.
DIAGNOSIS
- May present with low cardiac output, oliguria, & acidosis
- ACS is often overlooked. Diagnosis requires a high index of suspicion in patients who are at risk due to underlying disease (bowel ischemia) or who require extensive fluid resuscitation (e.g. severe pancreatitis, sepsis, major burns, etc)
- Unfortunately, physical exam is insensitive for ACS
- Imaging is poorly sensitive for ACS, though it may disclose the underlying cause (edema, ascites) or consequences of ACS (elevated diaphragm, flattened IVC, bowel enhancement)
Evacuate Intrabdominal Space-Occupying Lesions
Removal of intra-abdominal fluid can also reduce IAP
- Look for contributing ascites, blood and abscesses
- Consider ultrasound-guided bedside drainage
- Large, complex, or loculated may require IR/surgical drainage
MANAGEMENT
See WSACS guidelines for more