## Slide 1
by Nick Mark MD
non-invasive positive pressure ventilation
onepagericu.com
@nickmmark
Link to the most current version →
ONE
PURPOSE & DEFINITIONS:
Scalars correspond to pressure, flow, & volume waveforms
Non-invasive positive pressure ventilation (NIPPV) is a method of supporting ventilation and oxygenation. NIPPV can be used in acute respiratory failure to avoid endotracheal intubation. EPAP (expiratory pressure) = PEEP = CPAP
helmet
full face
partial face
nasal
Heater circuit
rate
16
VT
500
V3
8.5
PIP
22
ipap
15
epap
15
rate
12
FiO2
60
i time
1.0
rise
0
pH / PCO2 / PaO2 / HCO3 SpO2
VENTILATION
OXYGENATION
To increase the pH  increase the driving pressure (IPAP – EPAP)
To increase PaO2 / SpO2 adjust oxygenation parameters (FiO2 & EPAP)
ABG
Pulse Ox
May be more comfortable for CPAP or low pressure High air-leak. May cause pressure ulcers on nose. Pt can take oral meds easily.
INDICATIONS:
CONTRA-INDICATIONS:
Unresponsiveness/coma
Inability to trigger breath
Inability to protect airway / remove mask
Risk of emesis / copious secretions
Recent head/neck surgery
COPD exacerbation (↓intubation, ↓ mortality)
Cardiogenic pulmonary edema (↓ mortality)
Other causes of respiratory failure
DNI status
Extubation to NIPPV
Patients can tolerate higher pressures using masks than nasal interface. Full face masks are less likely than partial to cause pressure ulcers, & generally have less air-leak. Comfort is variable.
NIPPV contra-indicated?
Intubation indicated?
INTUBATE
Choose an appropriate interface
Choose a mode to correct the underlying problem
High air-leak / poor patient comfort?
reassess
Achieving oxygenation
& ventilation goals?
failure?
optimize
optimize
yes
no
LEAK
16
37
CC BY-SA 3.0
v1.1 (2021-05-30)
Mode | Description | Pro’s | Con’s | Ventilator settings / example | Monitor
CPAP Continuous positive airway pressure | Delivers a continuous pressure (CPAP == EPAP == PEEP) throughout the respiratory cycle, holding open collapsible airways and improving oxygenation. Patient triggers all breaths. | Improves oxygenation; relatively well tolerated. Useful in obstructive apneas, reduces intubations in CHF exacerbations. | Does not assist ventilation (risk of hypoventilation) | EPAP, FIO2 +8, 60% | Ventilation
S/T Spontaneous Timed (a.k.a BiLelel, BiPAP) | Sets, an inspiratory (IPAP) & expiratory pressure (EPAP). Every breath is supported with positive pressure. Patient triggers breaths, there is also a backup rate. (Similar to pressure support) | Improves ventilation & oxygenation. Useful in COPD to avert intubation & reduce mortality. May also reduce mortality in patients with immunosuppression presenting with hypoxemic respiratory failure. | Can have volutrauma | Backup RR, IPAP, Ti, Risetime, EPAP, FIO2 | Ventilation Volumes
 |  |  |  | 8 bpm, 16 cmH2O, 1 sec, 0.15 sec, +8, 60% | 
 | T - time/pressure/flow, C – flow, L - pressure |  |  | 12 bpm, 25 cmH2O, 0.9 sec, 0.15 sec, +8, 60% | 
AVAPS Adaptive volume assured pressure support (a.k.a. iVAPs) | Hybrid mode that dynamically adjusts inspiratory pressure (IPAP) to deliver a desired tidal volume. (Analogous to PRVC/VC+ modes) | Ensures minimum ventilation (within a desired pressure range). Not proven superior | Can have volutrauma With greater patient effort (e.g. gasping) will provide less support. | Backup RR, Goal TV, Pmin, Pmax, Risetime, PEEP, FIO2 | Ventilation pressures & volumes
 | T - time/pressure/flow, C – volume, L - volume |  |  | 8 bpm, 450cc, 10, 20, 0.15 sec, +8, 60% | 
(Not all NIPPV devices can be used with heater & humidifier)
May be better tolerated, may reduce the likelihood of requiring intubation, & decrease mortality. No risk of pressure ulcers.
Notes: Version 1.1 (corrected error on AVAPS description)