## Slide 1
by Nick Mark MD
oxygen delivery by mask
onepagericu.com
@nickmmark
Link to the most current version →
ONE
non-rebreather (nrb)
partial rebreather (pr)
simple mask (SM)
aka Hudson’s mask
flow 10 – 15 LPM
FiO2 ~80%
Oxygen Line
(100% oxygen)
Ambient air
(21% oxygen)
is entrained through the valve openings by the Venturi effect
Blended gas mixture (e.g. 31% oxygen)
mixture depends on flow rate & the size of the valve openings
PURPOSE:
Masks are often used to deliver supplemental O2, typically at higher flow rates & greater FiO2 than by nasal cannula.
The choice of mask often depends on how much supplemental O2 is required. The goal is provide the minimum necessary achieve the goal.
  In general, the goal SpO2 should be ≥94% in most people, or 88-92% in people at risk for hypercarbic respiratory failure.
The amount of oxygen delivered is approximate and can depend on many factors:
  Patient’s inspiratory effort (faster inspiratory flow will entrain more ambient air)
  Face seal (looser seal will entrain more ambient air)
Note that higher flow rates can rapidly deplete portable O2 tanks.
Non-rebreather masks have two one-way valves over the exhalation ports. These permitting exhalation but maintain a higher FiO2.
Note: this can be dangerous if the O2 supply is exhausted/interrupted!
Ambient air
is blocked from entering the mask (keeps FiO2 higher)
Carbon Dioxide
Can be exhaled freely (avoids rebreathing CO2)
venturi mask (VM)
face tent (FT)
v
Humidified Oxygen is produced by bubbling O2 through sterile water. Humidified O2 may be more comfortable for patients on higher flow rates (>4 lpm)
A venturi mask uses a small valve to mix oxygen & ambient air to achieve a desired FiO2. The venturi valves are color coded; each is sized to provide a different FiO2 for a specified flow rate:
Valve | Flow | FiO2
BLUE | 2 lpm | 24%
WHITE | 4 lpm | 28%
ORANGE | 6 lpm | 31%
YELLOW | 8 lpm | 35%
RED | 10 lpm | 40%
GREEN | 15 lpm | 60%
flow 2 – 15 LPM
FiO2 24-60%
flow 6 – 10LPM
FiO2 35-50%
flow 10 – 15LPM
FiO2 30 – 40%
flow 10 – 15 LPM
FiO2 60 – 80%
The addition of an inflatable reservoir increases delivered oxygen.
In the NRB this reservoir is filled with 100% oxygen.
In the PR this reservoir fills with a mixture of oxygen and exhaled air/CO2. This is why PR masks are seldom used.
See also Nasal Oxygen Delivery OnePager
Face Tents are loose fitting & may be useful in people who do not tolerate a tight-fitting mask (e.g. facial trauma, recent surgery, etc)
v1.0 (2022-08-11) CC BY-SA 3.0
Notes: Chest paper
https://journal.chestnet.org/article/S0012-3692(15)31420-3/fulltext