## Slide 1
by Nick Mark MD
pleural manometry
onepagericu.com
@nickmmark
Link to the most current version →
ONE
Measurement of Intrapleural Pressures and Pleural Elastance during therapeutic thoracentesis can be used to identify pleural pathologies such as trapped lung and entrapped lung and to predict successful pleurodesis.
It may also reduce the risk of re-expansion pulmonary edema.
Elastance
Normally Pleural Elastance is ≤ 14 cmH2O/L.
Pleural elastance > 14.5cmH2O/L suggests trapped lung.
Pleural elastance < 18 cmH2O/L predicts successful pleurodesis
+5
Connect a manometer (water column, pressure transducer, or digital manometer) behind a 3-way stopcock
Withdraw fluid using using a syringe and collecting bag as you would normally
Entrapped lung will initially have a slow decrease in IP followed by a rapid drop
Trapped lung
rapid drop in IP
Normal lung re-expansion steady slow decrease in IP
Measure the intrapleural pressure at end-expiration
intermittently (e.g. every 250cc) as fluid is removed by thoracentesis and calculate pleural elastance
Chart: 
| Normal re-expansion | Entrapped | Trapped
Cases | 68 | 18 | 14
Normal re-expansion occurs in the majority of cases
Entrapped Lung is an active inflammatory process. There is typically partial lung re-expansion
Exudative
Bimodal pressure change (initially slow pressure change, then rapid drop)
Normal or increased elastance
Treat the cause; drain the effusion dry if possible
Trapped Lung is a resolved inflammatory process with residual pleural fibrosis, which will prevent lung re-expansion
Transudatative (usually)
Linear pressure change
(rapid drop in pressure)
Increased elastance (>14.5 cmH2O/L)
Remove the rind preventing lung expansion (decortication)
10-15% of cases
15-20% of thoracentesis
v1.0 (2020-08-15)
pathology
fluid
manometry findings
treatment
Pleural elastance < 18 cmH2O/L (after 500 mL withdrawn) implies that the visceral and parietal pleura are opposed, and suggesting a successful response to pleurodesis in malignant effusions.
Avoid excessive negative pressure (<-20 cmH2O) during thoracentesis, as this can cause re-expansion pulmonary edema. However, the utility of pleural manometry to predict re-expansion pulmonary edema is controversial.
Consider stopping the thoracentesis if pressure drops < 20 cmH2O
Differentiate Entrapped Lung (partially inflatable) and Trapped Lung (un-inflatable)
PLEURAL PRESSURE MEASUREMENT:
INTERPRETATION:
DEFINITION:
1
2
3
Notes: Chest paper
https://journal.chestnet.org/article/S0012-3692(15)31420-3/fulltext