## Slide 1
exhalation
inhalation
SpO2
98
PI
0.8
by Nick Mark MD
capnography
onepagericu.com
@nickmmark
Link to the most current version →
ONE
colorimetric capnograph
CC BY-SA 3.0
v1.1 (2020-11-18)
Measurement of exhaled carbon dioxide can be used to confirm ETT placement, for safer procedural sedation, to guide resuscitation, and to monitor cardiac & pulmonary physiology.
· PETCO2 – End-tidal CO2 (what’s measured by capnography)
· PACO2 – Alveolar CO2
· PvCO2 – Mixed venous CO2
· PaCO2 – Arterial CO2 (what’s measured on an ABG)
PETCO2 is usually less than PaCO2 because of dead space. If physiological dead space increases the difference between PETCO2 and PaCO2 will also rise. Examples include:
· Low cardiac output – reduced delivery of CO2 to lungs
· Blockage of Pulmonary arteries (pulmonary embolus)
PRINCIPLE:
PaCO2
PvCO2
PACO2
PETCO2
45
35
40
40
ETCO2 in CARDIAC ARREST
ETT CONFIRMATION
Litmus paper changes color based on pH; exhaled CO2 lowers the pH and causes the the paper to transiently turn from PURPLE to YELLOW (“mellow yellow”); acidic vomitus can cause a false permanent color change.
A
B
C
Provides an approximate PETCO2 reading as each area is sensitive to different ETCO2 values:
A <4 mmHg
B 4-15 mmHg
C 15-38 mmHg
39
14
ETCO2
RR
portable electronic capnograph
waveform capnograph
ETCO2 (mmHg)
0
10
20
30
40
50
etCO2
39
RR
14
Side-stream detector
(longer latency)
I
II
III
IV
The waveform is composed of 4 phases
· Phase I – anatomical dead space ventilation
· Phase II – dead space mixed with alveolar ventilation
· Phase III – alveolar ventilation (where ETCO2 measured)
· Phase IV – end of exhalation
CAPNOGRAPH WAVEFORM :
ETCO2 in PROCEDURAL SEDATION
Measured PETCO2
IR spectroscopy precisely measures exhaled CO2 content
IR spectroscopy measures exhaled CO2 content and displays results graphically; can also be used with special nasal cannula to monitor non-intubated pts.
prolonged phase ii/iii
· Bronchospasm
· Airway obstruction
· COPD
cardiac oscillations
· Hypovolemia
· Hypoventilation
‘curare cleft’
· Patient dysynchrony during mechanical ventilation breath
dimorphic phase ii/ii
· Right mainstem intubation
· Differential lung emptying (Single lung transplant, severe kyphoscoliosis, etc)
prominent phase iv
· Obesity
· Pregnancy
· Poor compliance
sudden drop in etco2
· Displaced ETT
· Decreased CO (arrythmia, PE, etc)
Adequacy of CPR
· Achieving an PETCO2 > 20mmHg is associated with adequate CPR. If not achieving this goal consider rotating the person performing compressions.
Detection of ROSC
· Sudden increase in PETCO2 during CPR is a marker for ROSC.
Determination of futility
· Persistent PETCO2 < 10 for > 20 min is associated with futility, and even 5 min with ETCO2 < 10 is associated with poor outcomes.
Confirmation of exhaled CO2 can be used for ETT placement confirmation. Colorimetric capnograph is only appropriate in well perfusing patients; waveform capnograph is more accurate, particularly in low CO states.
SPECIFIC CAPNOGRAPH PATTERNS:
“shark fin”
Waveform capnography can be used to monitor for hypoventilation in non-intubated patients during procedural sedation (using an ETCO2 sensor nasal cannula). Waveform capnography is more sensitive than just SpO2 monitoring, and can detect hypoventilation up to 60 seconds before desaturation occurs.
· Poor gas exchange due to overdistension of alveoli – high TV, excessive PEEP, COPD
ETCO2 waveform
Peak ETCO2 value
Each heartbeat ejects a small amount of CO2
Terminal upswing
downsloping phase iii
· Severe emphysema
(alveoli destruction can cause rapid initial emptying of CO2)
Mainstream (in-line) detector
(Shorter latency)

## Slide 2
exhalation
inhalation
SpO2
98
PI
0.8
by Nick Mark MD
capnography
onepagericu.com
@nickmmark
Link to the most current version →
ONE
colorimetric capnograph
Measurement of exhaled carbon dioxide can be used to confirm ETT placement, for safer procedural sedation, to guide resuscitation, and to monitor cardiac & pulmonary physiology.
· PETCO2 – End-tidal CO2 (what’s measured by capnography)
· PACO2 – Alveolar CO2
· PvCO2 – Mixed venous CO2
· PaCO2 – Arterial CO2 (what’s measured on an ABG)
PETCO2 is usually less than PaCO2 because of dead space. If physiological dead space increases the difference between PETCO2 and PaCO2 will also rise. Examples include:
· Low cardiac output – reduced delivery of CO2 to lungs
· Blockage of Pulmonary arteries (pulmonary embolus)
PRINCIPLE:
PaCO2
PvCO2
PACO2
PETCO2
45
35
40
40
ETCO2 in CARDIAC ARREST
ETT CONFIRMATION
Litmus paper changes color based on pH; exhaled CO2 lowers the pH and causes the the paper to transiently turn from PURPLE to YELLOW (“mellow yellow”); acidic vomitus can cause a false permanent color change.
A
B
C
Provides an approximate PETCO2 reading as each area is sensitive to different ETCO2 values:
A <4 mmHg
B 4-15 mmHg
C 15-38 mmHg
39
14
ETCO2
RR
portable electronic capnograph
waveform capnograph
ETCO2 (mmHg)
0
10
20
30
40
50
etCO2
39
RR
14
Side-stream detector
(longer latency)
I
II
III
IV
The waveform is composed of 4 phases
· Phase I – anatomical dead space ventilation
· Phase II – dead space mixed with alveolar ventilation
· Phase III – alveolar ventilation (where ETCO2 measured)
· Phase IV – end of exhalation
CAPNOGRAPH WAVEFORM :
ETCO2 in PROCEDURAL SEDATION
Measured PETCO2
IR spectroscopy precisely measures exhaled CO2 content
IR spectroscopy measures exhaled CO2 content and displays results graphically; can also be used with special nasal cannula to monitor non-intubated pts.
prolonged phase ii/iii
· Bronchospasm
· Airway obstruction
· COPD
cardiac oscillations
· Hypovolemia
· Hypoventilation
‘curare cleft’
· Patient dysynchrony during mechanical ventilation breath
dimorphic phase ii/ii
· Right mainstem intubation
· Differential lung emptying (Single lung transplant, severe kyphoscoliosis, etc)
prominent phase iv
· Obesity
· Pregnancy
· Poor compliance
sudden drop in etco2
· Displaced ETT
· Decreased CO (arrythmia, PE, etc)
Adequacy of CPR
· Achieving an PETCO2 > 20mmHg is associated with adequate CPR. If not achieving this goal consider rotating the person performing compressions.
Detection of ROSC
· Sudden increase in PETCO2 during CPR is a marker for ROSC.
Determination of futility
· Persistent PETCO2 < 10 for > 20 min is associated with futility, and even 5 min with ETCO2 < 10 is associated with poor outcomes.
Confirmation of exhaled CO2 can be used for ETT placement confirmation. Colorimetric capnograph is only appropriate in well perfusing patients; waveform capnograph is more accurate, particularly in low CO states.
SPECIFIC CAPNOGRAPH PATTERNS:
“shark fin”
Waveform capnography can be used to monitor for hypoventilation in non-intubated patients during procedural sedation (using an ETCO2 sensor nasal cannula). Waveform capnography is more sensitive than just SpO2 monitoring, and can detect hypoventilation up to 60 seconds before desaturation occurs.
· Poor gas exchange due to overdistension of alveoli – high TV, excessive PEEP, COPD
ETCO2 waveform
Peak ETCO2 value
Each heartbeat ejects a small amount of CO2
Terminal upswing
downsloping phase iii
· Severe emphysema
(alveoli destruction can cause rapid initial emptying of CO2)
Mainstream (in-line) detector
(Shorter latency)
CC BY-SA 3.0
v1.1 (2020-11-18)